extrabee.org

---
What is a Radio Module?
- data in/out, RF in/out
- circuit board
- power supply/regulation
- micro-processor
- radio transceiver
- power amp for TX (some have this)
- low noise amp for RX (some have this)
- FCC certified (some have this)
- open-source

---
Applications for Radio Modules
- Arduino-to-Arduino communication
- Arduino-to-PC communication
- Medium range Raspberry
  Pi-to-device communication
- Serial cable replacement
- Digital I/O line passing
- Quad-rotors and other aircraft
- UAVs
- Robots
- Data loggers with remote access
- Wireless sensors
- Remote automation
- Mesh networks

---
EXTRABEE Hardware
TWI
CPU
USB
SPI
IRCOM
UART
DMAC
OSC
PLL
T/R
SW
DIV.
SW
BPF
ADC
AES/DES
DAC
FLASH
BPF
I/Q
MIX
BPF
ADC
GPIO
EEPROM
PWM
SRAM
Micro-processor
Radio Transceiver
Amplifier IC
Micro-processor
.4

---
Small Size
Dual Spatial-Diversity Antennas
POWER AMPLIFIER/LOW-NOISE AMPLIFIER ANTENNA DIVERSITY
POWER AMPLIFIER/LOW-NOISE AMPLIFIER ANTENNA DIVERSITY
RADIO TRANSCEIVER
MICRO-PROCESSOR

---
Three Antenna Options
WIRE MONOPOLE
ANTENNAS
EXTERNAL
ANTENNAS
INTEGRATED
ANTENNAS
SMALLEST,
SHORTEST RANGE
MOST EXPENSIVE,
LONGEST RANGE
INEXPENSIVE,
GOOD RANGE

---
Pin Signals
- Power, Ground
- Data in/out (USB, SPI, USART (w/ HW handshake), TWI)
- Reset
- 2 PWM outputs
- 8 GPIO
- 5 ADCs (12-bit, 2MSPS, internal or external VREF)
- 2 DACs (12-bit, built-in cal., internal or external VREF)
- RSSI
- IrDA port

---
Performance
- Operating Voltage: 2.1V to 3.5V
- TX power: 200mW (+23dBm)
- TX current 245mA @ 3.3V
- RX sens -100dBm (<1% PER, 250kbps)
- RX current 28mA (w/ LNA active)
- Sleep current < 5uA(depending on sleep mode)
- Range 100 ft – 2 miles (depends on antenna type and path type)
- Data rate 250kbps

---
RF Protocols
- The “language” spoken over-the air
- Incompatible devices cannot communicate with each other
- Popular ones:
  - Bluetooth
  - Wifi (IEEE 802.11...)
  - IEEE 802.15.4
  - Zigbee (802.15.4+mesh)
  - Z-Wave
  - WiMax
  - ISA100 (802.15.4+)
  - WirelessHART
  - 6LoWPAN
  - Many Proprietary Protocols

---
Configuration
- Sending “+++” invokes command mode
- “AT” command set – à la dial-up modem
- ATCH sets or reads the channel
- ATID sets or reads the network ID
- ATBD sets or reads the serial baud rate
- Configuration can be saved to EEPROM so it will be non-volatile

---
Open-Source Firmware
- Support and development community:
  - http://extrabee.org
- Source code hosted on Github:
  - http://github.com/extrabee/extrabee
- Present state:
  - Basic command mode interface
  - No bootloader yet, plan is to use an Arduino-compatible bootloader so it's easy to change the firmware

---
Development Environment
- AtmelStudio 6
  - AVR toolchain
  - GCC compiler

---
Prototype Range Test
City Park
1% PER

---
Prototype Range Test
Straight and Level Road with Traffic
40% PER

---
Prototype Range Test
Hillside Overlooking Valley
15% PER

---
Possible Future Features
- Arduino compatibility – run sketches right on the Extrabee module
- Packet sniffer mode
- I/O line passing
- RF channel scan command
- Serial API instead of data pass-through
- Encrypted packets over-the-air
- Over-the-air firmware updates

---
FCC Approval
- Any electronic device must be tested for FCC compliance for use in the US
- “Intentional Radiators” must not cause interference to other devices (FCC Part 15)
- Harmonics are generated at 2x, 3x, 4x... the main operating frequency
- A test lab verifies that the device complies with FCC limits and issues a certificate
- Testing is expensive

---
Kickstarter for FCC Test
- Kickstarter campaign to pay for FCC test
- The software is already open-source
- Stretch goal on Kickstarter makes the hardware open-source too
- http://kickstarter.extrabee.org

---
Demonstration

---
Need Help?
Visit Our User Forum: extrabee.org
Follow @ExtraBee on Twitter